## Slide 1: RCDC SLIDES README
Font Issues
  To ensure that the RCDC logo appears correctly on all computers, it is represented with images in this presentation. This looks fine but cannot, of course, be edited.
  The “AC-DC” font used for the logo is called Squealer, and the font’s license allows for free use, but does not allow embedding into editable documents (like powerpoint). If you want the font, you can download and install it for free from: http://new.myfonts.com/fonts/larabie/squealer/
  If this text: RC*DC looks like this picture: then you have the Squealer font installed correctly.

## Slide 2: Relaxed Consistency Deterministic Computer
Joseph Devietti, Jacob Nelson, Tom Bergan Luis Ceze, Dan Grossman
“deterministic deeds, done dirt cheap”
Notes: I’m here to present RCDC, a r.c.d.c with a new deterministic consistency model that improves performance, and a new hybrid hw/sw design that lowers complexity compared to previous work. Research done with …
We all know that the multicore era is in full swing, that multicores are difficult to program, and that nondeterminism is one of the key reasons for such difficulty. In contrast to today’s nondeterministic machines, a deterministic multiprocessor design (like the one I’ll show you today), has the potential to radically improve the way we develop parallel software.

## Slide 3
Debug
reverse debugging is possible
Deploy
more robust production code
Test
no need to
stress test
testing results
are reproducible
production bugs
can be reproduced
in-house
tested inputs behave
identically in production
determinism
improves the software development cycle
record-and-replay
determinism
Notes: a deterministic multiprocessor design (like the one I’ll show you today), has the potential to radically improve the way we develop parallel software.
rr (e.g. DoublePlay) can provide some of these benefits

## Slide 4: determinism
Debug
Deploy
Test
improves the software development cycle
Notes: there’s concrete evidence that this kind of rep is valuable, in the number of commercial tools that provide rep
all current tools help with debugging or testing…
…except Halo 2 (2004). Halo 3 (2007) leverages determinism for the Saved Films feature
To understand the benefits of RCDC, we need to touch on related work in deterministic execution.

## Slide 5: History of Deterministic Execution
Kendo [ASPLOS ‘09]
Grace [OOPSLA ‘09]
Deterministic Execution for Restricted Programs
DMP [ASPLOS ‘09]
CoreDet [ASPLOS ‘10]
dOS [OSDI ‘10]
Determinator [OSDI ‘10]
Calvin [HPCA ‘11]
[ASPLOS ‘11]
Deterministic Execution for Arbitrary Programs

## Slide 6: History of Deterministic Execution
DMP [ASPLOS ‘09]
seq. consistency
total store order
DRF0 [ISCA ‘90]
CoreDet [ASPLOS ‘10]
Calvin [HPCA ‘11]
dOS [OSDI ‘10]
Determinator [OSDI ‘10]
"Piled Higher and Deeper" by Jorge Cham www.phdcomics.com
Jorge Cham © 2008
WO
RC
[ASPLOS ‘11]
Notes: let look at these techniques wrt their memory consistency models, we’ll see that consistency has been steadily relaxed over time
sc => tso: improve scalability while avoiding the complexities of speculation
tso => drf0: improved perf, RCDC offloads some imp’l complexity to sw

## Slide 7: Contributions
2
3
4
1
Dmp-HB
a new deterministic consistency model based on DRF0 with improved performance
a low-complexity hw/sw deterministic execution system
hw: store buffers and instruction counting
sw: everything else
C/C++ compiler based on LLVM,
runs on commodity multicore
hardware simulation using Pin
Outline
Notes: Our model is more relaxed than conventional hw memory models like TSO, WO and RC.
Relaxing the consistency model alone is insufficient to improve upon prior work; we had to optimize the implementation of deterministic sync as well.

## Slide 8: starting simple: serialization
quantum
deterministic quantum size
+
deterministic scheduling
determinism
quantum round
threads
time →
T1
T2
T3
Notes: before we can understand rcdc, we need to understand a bit about how we can force arbitrary parallel programs to execute deterministically.
this is det given that quanta are a det size, and that we switch between threads in a det way

## Slide 9: recovering parallelism with Dmp-TSO
parallel mode: buffer all stores (no communication)
commit mode: deterministically publish buffers
serial mode: for atomic ops
time →
T1
T2
T3
commit
parallel
serial
lock A
lock B
wr A
rd A
rd A

## Slide 10: Why is Dmp-TSO slow?
time →
commit
parallel
serial
serialization
imbalance
T3
T1
T2
Kendo [ASPLOS ‘09]

## Slide 11: Why is Dmp-TSO slow?
time →
commit
parallel
T3
T1
T2
serialization
imbalance
Kendo [ASPLOS ‘09]
Dmp-HB
parallel-mode synchronization
complements
relaxed consistency

## Slide 12: synchronization in parallel mode with Kendo
instruction count →
T1
T2
T3
[Olszewski et al., ASPLOS ‘09]
lock A
thread with globally min insn count can do atomic op
T2 not globally min insn count
T2 is globally min insn count

## Slide 13: Why is Dmp-TSO slow?
time →
commit
parallel
serial
serialization
imbalance
T3
T1
T2
Kendo [ASPLOS ‘09]

## Slide 14: Why is Dmp-TSO slow?
time →
commit
parallel
T3
T1
T2
serialization
imbalance
Dmp-HB
Kendo [ASPLOS ‘09]

## Slide 15: DRF0: happens-before consistency
happens-before edges defined by synchronization operations
remote updates visible via cross-thread happens-before edges
SC for DRF programs
upholds C++/Java memory models
programmer-visible model doesn’t change
[Adve and Hill, ISCA ‘90]

## Slide 16
relaxed consistency (DRF0)
sync in parallel mode (Kendo)
Dmp-HB
deterministic scheduling (DMP)

## Slide 17: Dmp-HB : happens-before determinism
time →
T1
T2
T3
commit
parallel
lock A
lock B
unlock A
lock A
TSO
RC
no serial mode
less imbalance
DRF0
explicit fence iff inter-thread HB edge doesn’t cross commit
explicit fences rarely necessary

## Slide 18: Outline
2
3
4
1
Dmp-HB
a new deterministic consistency model with improved performance
a low-complexity hw/sw deterministic execution system
hw: store buffers and instruction counting
sw: everything else
C/C++ compiler based on LLVM,
runs on commodity multicore
hardware simulation using Pin

## Slide 19: Architecture
L2$
Core
L1$
Store Buffers in Private $
StoreToSB
CommitSB
SaveSB
RestoreSB
Precise Insn Counting
StartInsnCount
StopInsnCount
ReadInsnCount
Core
L1$
Traps
SBFull
QuantumReached
application/OS can
choose nondeterminism
align context switches with quantum boundaries
runtime system
Notes: no speculation

## Slide 20: Outline
2
3
4
1
Dmp-HB
a new deterministic consistency model with improved performance
a low-complexity hw/sw deterministic execution system
hw: store buffers and instruction counting
sw: everything else
C/C++ compiler based on LLVM,
runs on commodity multicore
hardware simulation using Pin

## Slide 21: Experimental Setup
structure | size | access latency
private L1 | 8-way, 32KB | 1 cycle
private L2 | 8-way, 256KB | 10 cycles
shared L3 | 16-way, 8MB | 35 cycles
memory | - | 120 cycles
Pin-based simulator
1 IPC, except for memory ops
PARSEC v2.1 with simsmall inputs
extended CoreDet C/C++ compiler [ASPLOS ‘10]
8-core Intel Harpertown @ 2.8GHz, 10GB RAM
PARSEC v2.1 with simlarge inputs

## Slide 22: Simulation: Overheads
Chart: % overhead compared to nondet
| blacksch | dedup | ferret | fluid | streamcl | swaptions | vips | x264
2p | -0.01525 | 0.047152 | 0.11498 | 0.14779 | 0.094515 | 0.018232 | 0.14293 | 0.03948
4p | 0.045871 | 0.046393 | 0.29256 | 0.20849 | 0.19884 | 0.12173 | 0.20593 | 0.12365
8p | 0.25728 | 0.054841 | 0.52269 | 0.28612 | 0.61957 | 0.2517 | 0.28535 | 0.16801
16p | 0.16504 | 0.031491 | 0.65462 | 0.26056 | 0.63378 | 0.32331 | 0.21487 | 0.082105
overhead < 60% in worst case
50k
50k
25k
1k
1k
50k
50k
50k
quantum size
(insns)

## Slide 23: Compiler: Dmp-HB vs. Dmp-TSO
Chart: % overhead compared to nondet
| 2 | 4 | 8 | 2 | 4 | 8 | 2 | 4 | 8 | 2 | 4 | 8
hb | 0.072884 | 0.076952 | 0.088982 | 1.3381 | 1.3626 | 1.4647 | 2.4297 | 2.2769 | 2.9084 | 1.5105 | 1.9663 | 2.4903
tso | 0.070725 | 0.07325 | 0.086925 | 1.2761 | 1.3531 | 1.5012 | 2.7227 | 2.957 | 4.0497 | 2.0354 | 2.6258 | 3.4317
blackscholes
fluidanimate
fmm
swaptions
threads
200k
200k
50k
50k
quantum size
(insns)

## Slide 24: Conclusions
Dmp-HB: a new deterministic consistency model
: a new deterministic multiprocessor design
  no speculation
  lightweight hardware support
Relaxed consistency is a natural optimization for determinism
source code and data available at http://sampa.cs.washington.edu

## Slide 25: Thanks!
Questions?
source code and data available at http://sampa.cs.washington.edu
Notes: possible questions:
how does this work with SMT? (need to partition sb/$, not elegant)
compare to Calvin?
how do you know this is DRF0?
TODO: quantum size sensitivity chart?

## Slide 26: DRF0 hardware requirements [ISCA ‘90]
Intra-processor dependencies are preserved.
All writes to the same location can be totally ordered based on their commit times, and this is the order in which they are observed by all processors.
All synchronization operations to the same location can be totally ordered based on their commit times, and this is also the order in which they are globally performed. Further, if S1 and S2 are synchronization operations and S1 is committed and globally performed before S2, then all components of S1 are committed and globally performed before any in S2.
A new access is not generated by a processor until all its previous synchronization operations (in program order) are committed.
Once a synchronization operation S by processor Pi is committed, no other synchronization operations on the same location by another processor can commit until after all reads of Pi before S (in program order) are committed and all writes of Pi before S are globally performed.